La BlueFrog-V1
Rel-2.0_KickStart_V1
Low-level API Contents

Custom Type Definitions :

(from file custom_types.h)

typedef enum {
  FALSE = 0,
  TRUE = 1
}
boolean_t;

On-board LEDs and Slider Switch Control:

(from file LBF_LED+Switches_lowlevAPI.h)

void Red_Led_ON(void);
void Red_Led_OFF(void);
void Red_Led_TOGGLE(void);
void Green_Led_ON(void);
void Green_Led_OFF(void);
void Green_Led_TOGGLE(void);

boolean_t Get_Slider_Select1(void);
boolean_t Get_Slider_Select2(void);

Data Flash Control :

(from file LBF_FLASH_lowlevAPI.h)

void FLASH_EraseBulk(void);
void FLASH_WritePage(uint8_t* pBuffer, uint32_t WriteAddr, uint16_t NumByteToWrite);
void FLASH_WriteBuffer(uint8_t* pBuffer, uint32_t WriteAddr, uint32_t NumByteToWrite);
void FLASH_ReadBuffer(uint8_t* pBuffer, uint32_t ReadAddr, uint32_t NumByteToRead);
uint32_t FLASH_ReadID(void);

Direct STM32 GPIO Control :

(from file LBF_GPIO_lowlevAPI.h)

#define GPIO_HIGH(PORT,PIN) …......
#define GPIO_LOW(PORT,PIN) …......
#define GPIO_TOGGLE(PORT,PIN) …......

OLED Control :

(from file LFB_OLED_lowlevAPI.h)

#define OLED_CS_LOW() …....
#define OLED_CS_HIGH() …....
#define OLED_RS_LOW() …....
#define OLED_RS_HIGH() …....
#define OLED_RESET_LOW() …....
#define OLED_RESET_HIGH() …....

/* Colors for OLED in rgb565 format */
#define BLACK 0x0000
#define WHITE 0xFFFF
#define RED 0xF800
#define GREEN 0x07E0
#define BLUE 0x001F
#define YELLOW 0xFFE0
#define CYAN 0x07FF
#define LIGHT_BLUE 0x1C9F
#define ORANGE 0xFD20

/* OLED SPI */
uint8_t OLED_SPI_TransferByte (uint8_t octet);
void OLED_SendCmd (uint8_t Value);
void OLED_SendData (uint16_t Value);
void OLED_WriteReg (uint8_t RegName, uint8_t RegValue);
void OLED_DataStart (void);
void OLED_DataEnd (void);

/* OLED Gfx Generation */
void OLED_SetRegion(uint8_t x, uint8_t y, uint8_t width, uint8_t height);
void OLED_Fill(uint8_t x, uint8_t y, uint8_t width, uint8_t height, uint16_t color565);
void OLED_DisplayBuffer(uint8_t x, uint8_t y, uint8_t width, uint8_t height, uint16_t *buffer);
void OLED_Clear (void);

Power Management

(from file LBF_PWR_lowlevAPI.h)

void Turn_VDDH_On(void);
void Turn_VDDH_Off(void);
boolean_t Check_VDDH_On(void);

UART#1 Control

(from file LBF_UART1_lowlevAPI.h)

void UART_SendData (uint8_t data);
uint8_t UART_ReceiveData (void);
void UART_SendString(char* pString);

Services

(from file Services.h)
void Delay_ms (volatile uint32_t nTime);